| Models 1010KVH / 1210 KVH Ka-Band Mobile VSAT IP Broadband Antenna Systems |
| --- |
| Key Features | Highly Efficient Motorized Antennas |
|  | Zero Backlash AvL Cable Drive |
|  | Auto-Acquisition Controller |
| Standard Feed | Commercial Ka-Band |
| Reflector Sizes | 1.0m or 1.2m (future option for 85cm) |
| Configurations | Vehicle-Mount |
|  | Fly&Drive |
|  | FlyAway – Case-Based or Tripod |
| Market Solutions | Mobile Broadband Internet Access |
|  | Satellite News Gathering |
|  | Disaster Relief |
|  | Oil & Gas Data Backhaul |
|  | Defense & Homeland Security |
| Operates With | HughesNet |
| Mechanical |
| Az/El Drive | Motorized AvL Zero Backlash Cable Drive (Patent Pending) |
| Polarization | RHCP/LHCP Pol Select Option Available |
| Reflector Construction | Single Piece Carbon Fiber |
| Axis Travel Azimuth | 400° (±200°) |
| Elevation | 0-90° antenna bore sight (true elevation from calibrated inclinometer) |
| Az/El Speed Slewing/Deploying | Typical: Elevation 0.1°/second, Azimuth 2º/second |
| Motors | 24 VDC Variable Speed, Constant Torque |
| Interface | Type F connector(s) at antenna base or 25 ft. (7.6m) Coax from Base |
| Electrical Interface | One 25 ft. (7.6m) cable with connector from base connector panel to controller |
| Manual/Emergency Drive | Hand crank for az and el axes |
| Time to Acquisition | Less than 15 minutes; 8 minutes typical |
|  | 85cm Antenna | 1.0m Antenna | 1.2m Antenna |
| Stowed Dimensions | 53 L x 36 W x 13½ H inches (135 L x 91 W x 34 H cm) | 61.5 L x 40 W x 15 H inches (156 L x 102 W x 38 H cm) | 69 L x 48 W x 16.3 H inches (174 L x 122 W x 41 H cm) |
| Weight (approximate – depends on options selected) | 90 lbs. (41 kg) typical | 111 lbs. (50 kg) typical | 130 lbs. (59 kg) typical |
| Environmental |
|  | 85cm Antenna | 1.0m Antenna | 1.2m Antenna |
| Wind – Survival Deployed | 80 mph (129 kph ) | 80 mph (129 kph) | 80 mph (129 kph ) |
| Stowed | 100 mph (161 kph) | 100 mph (161 kph) | 100 mph (161 kph) |
| Wind – Operational | 45 mph (72 kph) | 45 mph (72 kph) | 45 mph (72 kph) |
| Pointing Loss in Wind - Ka (Rx) |  |  |  |
| 30 mph gusting to 45 mph (48 kph gusting to 72 kph) | 1.0 dB typical | 1.0 dB typical | 1.0 dB typical |
| Temperature: Operational | -25° to 125° F (-32° to 52° C) | -25° to 125° F (-32° to 52° C) | +5° to 125° F (-15° to 52° C) |
| Survival | -40° to 140° F (-40° to 60° C) | -40° to 140° F (-40° to 60° C) | -40° to 140° F (-40° to 60° C) |

Models 1010KVH / 1210 KVH Ka-Band Mobile VSAT IP Broadband Antenna Family

| RF/Electrical |
| --- |
| Reflector Size ► | 85 cm (future option) | 1.0m | 1.2m |
| RF Parameter ▼ | Receive | Transmit | Receive | Transmit | Receive | Transmit |
| Frequency Range (GHz) | 19.7 - 20.20 | 29.5 - 30.0 | 19.7 - 20.20 | 29.5 - 30.0 | 19.7 - 20.20 | 29.5 - 30.0 |
| Polarization Configuration | RHCP or LHCP | RHCP or LHCP | RHCP or LHCP |
| Gain (mid-band) @ Horn Interface (dBi) | 43.1 | 46.6 | 44.5 | 48.0 | 46.1 | 49.6 |
| G/T (mid-band, clear horizon) assuming 100 K LNB (dB/K) | 19.8 |  | 21.2 |  | 22.8 |  |
| Beam width (degrees) -3 dB | 1.2 | 0.8 | 1.1 | 0.7 | 0.9 | 0.6 |
| -10 dB | 2.3 | 1.5 | 1.9 | 1.3 | 1.6 | 1.1 |
| Radiation Pattern Compliance | ITU-R S.580.6 | ITU-R S.580.6 | FCC 25.209, ITU-R S.580.6 |
| Antenna Noise Temperature (midband) | 109 K |  | 107 K |  | 107 K |  |
| Power Handling Capability |  | 50W |  | 50W |  | 50W |
| VSWR @ Horn Interface | 1.30:1 | 1.30:1 | 1.30:1 | 1.30:1 | 1.30:1 | 1.30:1 |
| Reflector Optics | 0.7 f/D | 0.8 f/D | 0.8 f/D |
| Feed Type | Integral Feed/ Polarizer/OMT/Transceiver | Integral Feed/ Polarizer/OMT/Transceiver | Integral Feed/ Polarizer/OMT/Transceiver |
| Axial Ratio | Feed Dependent | Feed Dependent | Feed Dependent |
| Cross-Polarization Isolation | Feed Dependent | Feed Dependent | Feed Dependent |
| Feed Port Isolation – Tx to Rx | Feed Dependent | Feed Dependent | Feed Dependent |
| Controller |
| Controller ► | AvL AAQ |
| Features | AvL one button auto-acquisition of selected satellites, including peaking and optimization of cross pol. Internal movement detector and automatic stow. Optional hand-held control and separate power supply. Certified for auto-commissioning on most satellite services. |
| Size | Embedded ACU with separate 1 Rack Unit Controller Interface Panel (CIP) power supply with LCD and keypad. 250 W and 500 W (1.6m and larger antennas) versions available. |
| CIP Input Power | 120/240 VAC 60/50 Hz, 6/3 A Max. Power consumption is antenna size dependent: During acquisition 150 W or 300 W is typical, ~ 50 W Idle |
| Available Options, Upgrades & Services |
| Optional 2-Port Ku-band Precision (standard Cross-Pol comp.) or Mode-Matched (enhanced Cross-Pol comp.) Feed Optional Ku-Band BUC mounting Future option for 85cm reflector Optional controller upgrade to 1RU with display Upgrade to Custom RF/IF I/O cabling configurations available Custom Colorization (contact factory for available colors) Add Custom Logo on Reflector Face (1- or 2-Color; per AvL Logo Policy) Optional aerodynamic cowling Spare Parts Kit |