| Model 2400 C-Band/Ku-Band SNG 2.4m Motorized Transportable Vehicle-Mount Antenna |
| --- |
| Unique Features | 2.4m AvL Single Piece Carbon Fiber Reflector |
|  | Optional three-piece carbon fiber reflector with manually folding hinged wings or motorized folding hinged wings |
|  | Zero Backlash AvL Cable Drive |
|  | Compact/Rugged Pol Gear Drive |
|  | “One-Button” Auto-Acquisition |
| Optics | Offset, Prime Focus, 0.8 f/D |
| Standard Rx/Tx Feed | Either 2-Port Ku-Band Precision (LP) (standard Cross-Pol comp.) or 2-Port C-Band (CP or LP), Standard Band or INSAT Band |
| Optional Feeds | 4-Port Ku-Band Precision (LP) (standard Cross-Pol comp.) |
|  | 2-, 3- or 4-Port Ku-Band Wideband (LP) |
|  | 3-, 4-Port C-Band (CP or LP) |
|  | 2-Port Extended C-Band (LP) |
| Polarization Adjustment | Motorized Worm Gear Drive |
| Standard Colorization | AvL White or Metallic Gray (optional colors available) |
| Mechanical |
| Az/El Drive | Motorized Zero Backlash AvL Cable Drive (Patent Pending) |
| Polarization Drive System | Motorized Worm Gear Drive |
| Reflector Construction | 2.4m Single Piece AvL Carbon Fiber; Optional three-piece carbon fiber reflector with manually folding hinged wings or motorized folding hinged wings |
| Axis Travel |  |
| Azimuth | ±200° Standard; 270° with dual waveguide to vehicle, options include dual Ku, single C + single Ku. Special dual waveguide ±200° available (rotary joints protrude into vehicle further than standard) |
| Elevation Mechanical | 0°-90° of reflector bore sight |
| Electrical | 5° to 90° Standard limits or 5° to 65° (CE Approval) |
| Polarization | ±95° for 2-port and 3-port Feeds; ±50° for 2-port Wideband and 4-port Feeds |
| Az/El Speed |  |
| Slewing/Deploying (typical) | 1°/second Az, 1°/second El |
| Peaking (typical) | 0.2°/second |
| Motors | 24 VDC Variable Speed, Constant Torque |
| RF Interface |  |
| HPA Mounting | Feed Boom, Rear of Reflector or Inside Truck |
| Axis Transition | Twist-flex or optional rotary joints for Ku-Band; Pol rotary joint standard for C-Band |
| Waveguide | Cover Flange at Interface Point |
| Coax | RG59 run from feed to base plus 25 ft. (8m); Option for 50 ohm LMR-240 |
| Electrical Interface | 25 ft. (8m) Cable with Connectors for Controller |
| Manual/Emergency Drive | Hand crank on Az, El and Pol axes |
| Time to Acquisition | Less than 15 minutes, 8 minutes typical |
| Weight (approximate) | 550 lbs. (250 kg) with Ku Feed and AAQ Controller |
| Stowed Dimensions | 123.5 L x 96.0 W x 24.2 H in (314 L x 244 W x 62 H cm) (may vary with CFE or 3-,4-port C-band) |
| Environmental |
| Wind – Survival | Deployed: 70 mph (113 kph); Stowed: 100 mph (161 kph) |
| Wind – Operational | 45 mph (72 kph), gusts to 60 mph (97 kph) |
| Pointing Loss in Wind* | C-Band Rx | Ku-Band Rx |
| 30 mph gusting to 45 mph (48 kph gusting to 72 kph) | 0.2 dB Typical | 0.6 dB Typical |
| Temperature: |  |
| Operational | -22° to 125° F (-30° to 52° C) |
| Survival | -40° to 140° F (-40° to 60° C) |
| Shock and Vibration | Designed for transport via rough Roads, Rail, Sea and Air |
| Corrosion Protection | For all regions from coastal to industrial, some periodic maintenance required for appearance |
| Humidity, Rain, Blowing Sand | Sealed to withstand 0-100% with condensation, >4 inches/hour (102 mm/hr.), blowing to 40mph |

| Model 2400 C-Band/Ku-Band SNG 2.4m Motorized Transportable Vehicle-Mount Antenna |
| --- |
| RF/Electrical |
| Feed Type ► | With. 2-Port C-Band | With. 2-Port Precision Ku-Band |
| RF Parameter ▼ | Receive | Transmit | Receive | Transmit |
|  | Standard | INSAT | Standard | INSAT |  |  |
| Frequency Range (GHz) | 3.625 - 4.2 | 4.50 – 4.80 | 5.850 - 6.425 | 6.725 – 7.025 | 10.95 - 12.75 | 13.75 - 14.50 |
| Polarization Configuration | Linear or Circular Options | Linear | Linear or Circular Options | Linear | Linear Orthogonal Standard, Optional Co-Pol |
| Gain (midband) (dBi) | 38.0 | 39.2 | 41.8 | 42.6 | 47.0 | 48.8 |
| Beam width -3 dB (Degrees) | 2.2 | 1.9 | 1.4 | 1.3 | 0.7 | 0.6 |
| -10 dB (Degrees) | 4.0 | 3.4 | 2.6 | 2.3 | 1.3 | 1.1 |
| Radiation Pattern Compliance | FCC §25.209, ITU-R S.580.6, IESS 207 | ITU-R S.580.6 | FCC §25.209, ITU-R S.580.6, IESS 207 | ITU-R S.580.6 | FCC §25.209, ITU-R S.580.6, IESS 208 |
| Antenna Noise Temperature @ 20° El | 49°K | 48°K | - | - | 61° K | - |
| G/T, Midband (dB/°K) | 19.5 dB/˚K w/ 20°K LNB | - | - | - | 26.5 dB/˚K w/ 50°K LNB |  |
| VSWR | 1.30:1 | 1.30:1 | 1.30:1 | 1.30:1 | 1.30:1 | 1.30:1 |
| Power Handling Capability | - | - | 1000 watts per Port | - | - | 1000 watts per Port |
| Circular Axial Ratio (within pointing cone) (dB) | 2.3 | - | 1.3 | - | - | - |
| Cross-Polarization Isolation (dB) |  |  |  |  |  |  |
| On-Axis | 35 | 35 | 35 | 35 | 35 | 35 |
| Off Axis (within 1 dB BW) | 30 | 30 | 30 | 30 | 28 | 30 |
| Feed Port Isolation – Tx to Rx (dB) | 65 dB | 35 dB | 105 dB | 70 dB | 35 dB | 80 dB |
| Controller |
| Standard Controller ► | Three-Axis Jog Control & Display with Auto-Stow |
| Optional Upgrades |  |
| Semi-automatic Operation | Drive to calculated position based on operator entered vehicle location, heading, plus satellite (longitude or listed) |
| Automatic Operation | Drive to calculated position based on auto GPS and Flux-Gate Compass data and satellite peaking with LNB signal |
| Auto-acquisition | One-button acquisition of selected satellite including peaking and optimization of cross-pol (certified for auto- commissioning on most satellite services) |
| Size | Two Rack Units for Semi-automatic & Automatic Controllers |
| Input Power | 110/240 VAC, 1 phase, 50/60 Hz, 10/5 A peak, 1 A continuous |
| Controller ► | AvL AAQ |
| Features | AvL one button auto-acquisition of selected satellites, including peaking and optimization of cross pol. Internal movement detector and automatic stow. Optional hand-held control and separate power supply. Certified for auto-commissioning on most satellite services. |
| Size | Embedded ACU with separate 1 Rack Unit Controller Interface Panel (CIP) power supply with LCD and keypad. 250 W and 500 W (1.6m and larger antennas) versions available. |
| CIP Input Power | 120/240 VAC 60/50 Hz, 6/3 A Max. Power consumption is antenna size dependent: During acquisition 150 W or 300 W is typical, ~ 50 W Idle |
| Available Options, Upgrades & Services |
| Optional feeds: 4-port Ku-band Precision (LP), 2-, 3- or 4-port Ku-band Wideband (LP), 2-Port C-Band (CP or LP), 3-, 4-port C-band (CP & LP) Add co-polarization kit (for 2-port wideband Ku feeds only) − configures Rx and Tx to same polarity Optional waveguide rotary joint with flex on pol axis for Ku-Band Optional H/V switch (Ku Wideband) Optional wave guide cross axis kits Optional Dual/Redundant HPA high power integration Mounting Pallet (adds 4.5” (11.4 cm) to stow height) | Add BUC/HPA mounting (NOTE: minimum elevation may be restricted by these options)Upgrade to custom RF/IF I/O cabling configurations available Optional coax cables available Custom colorization (contact factory for available colors) Add custom logo on reflector face (1- or 2-Color; per AvL Logo Policy) Spare parts kit Beacon receiver – inclined orbit tracking – resolvers/upgrade 3-piece reflector for 72 inch Stow Width (motorization optional) |

* Assumes stable platform